## Slide 1: 3D Printing
3D Printing
Barry H Ginsberg, MD, PhD

## Slide 2: 3D Printing
Printing in Plastic
Printing in Metal
Printing Other Materials

## Slide 3: Printing in plastic
Stereolithography
  First 3D printers, 1980’s
  Use light-sensitive liquid polymer in Vat (dark)
  Hardens with light
  Platform/Elevator just below top of plastic
  Write on with laser
  Lower platform
  Repeat

## Slide 4: Printing in plastic
Stereolithography
  Machines big and expensive ($250K)
  Polymer $800/gal (~$100/kg)
  Only limit on printing is that layers need to be attached
  Generally only used in industry

## Slide 5: Desktop 3D SLA
Desktop 3D printer
~$3500
Resin $150 vat

## Slide 6: Printing in plastic
Stereolithography
  Early plastics were not robust, now better.
  Models to: Show consumers Show management Test for function Test for ease of use

## Slide 7: Software, Modeling and language
Need a CAD program, 123D Design
Create the object from primitives (cubes, rods, freehand, polylines)
Save the CAD file
Export as a STL file (STereolithography Language)

## Slide 8: Software, Modeling and language
STL is a subset of G-code (used for all CAM)
Creates layers
The CAM program will read the STL file and adapt
Will add support if necessary

## Slide 9: Software, Modeling and language

## Slide 10: Software, Modeling and language

## Slide 11: 3D Extruder video (ces)

## Slide 12: 3D Extruders
Heat plastic filament to >200 C (>400 F)
Force through a nozzle to 0.4 mm (0.016 in)
Move back and forth like a plotter, laying down plastic
Raise head 0.2 mm and repeat laying down plastic

## Slide 13: 3D Extruders
Print head (x axis)
Elevator (z axis)
Plate (y axis)
Filament
Feeder

## Slide 14: 3D Extruders
Slow
Pencil holder about 4 hours
About 25 cents in plastic

## Slide 15: Some of my projects

## Slide 16: Some more of my Projects

## Slide 17: Buying a 3d printer
3D printers are not expensive ($500-2500). I paid $2500 for my first laser printer ($5000 in today’s dollars)
They don’t required too much computer power (although the CAD may)
But they require frequent repairs that you have to do yourself.
Thus, I think they are not ready for prime time, but hobbyists can have a lot of fun with them
$300
$500
$700
$2500

## Slide 18: 3D Printing in metal (Praxa)

## Slide 19: 3D Printing in metal
Sintering metal powder with laser (strong)
Gluing metal powder with print head (needs bronze infusion)
Melting metal powder with laser (very strong)
Metal extrusion (1000-2600 F). Metal powder, laser, base/hotend on gimbals
Metal extrusion, metal nanoparticles, laser, can produce unsupported

## Slide 20: 3D Printing in metal (beam)

## Slide 21: 3D Printing, other
Printing a hand

## Slide 22: 3D printing, other
Ceramics, using clay
Cake decorating Tissue scaffolding
  Bone
  Cartilage
  Flexible
    Blood vessels
    Gut

## Slide 23: 3d Printing, other
Airbus 350 has >1000 3D printed parts
3D printed structures